## Slide 1: User Interface Design and Implementation of Velmex BiSlide Motor and EMD High Voltage Generator Control for X-Ray Diffraction System
Mridu Nanda1, Anuj J. Kapadia2
1North Carolina School of Science and Math, Durham, NC
2Carl E. Ravin Advanced Imaging Laboratories, Duke University, Durham, NC
Notes: //give project summary

## Slide 2
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Traditional x-ray technique
Material content?
Notes: When a photon collides with an atom, the atom my absorb the photons energy by boosting an electron to a higher level
Here we have an x-ray produced by traditional x-ray techniques
1) A very concentrated beam of photons onto a metal film
2) The soft tissue (skin & organs cannot absorb energy and the beam passes through them)
3) Black areas on an X-ray represent areas where the X-rays have passed through soft tissues. White areas show where denser tissues, such as bones, have absorbed the X-rays
http://science.howstuffworks.com/x-ray1.htm
These x-ray DISCARD x-ray scatter (results from ___?) which degrades image quality
- //write notes
http://www.sprawls.org/ppmi2/INTERACT/
(image is of lung cancer)
Identify materials?  Attenuation coefficients
- how easily x-ray can pass through material
- matching the

## Slide 3
X-ray diffraction system
  Applications?
    Medical screening, Homeland security
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Notes: //ask kapadia for clearer picture!!
Resulting x-ray of cancerous breast tissue: different color pixels = different tissue types (white = air, black = cancerous, red = normal, magenta = fibroglandular, blue = adipose)

## Slide 4
Goal: Create a streamlined user-friendly interface through LABVIEW programming language
Velmex BiSlide Motors
EMD High Voltage Generator
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Notes: Why labview?
- easy to communicate via serial communication (NI-VISA)
- purposed for device instrumentation (also does not require instrument drivers)
Explain serial communication: format (start data, stop), baud rate, parity
Also mention rs-232 protocol: physical and electrical characteristics of serial communication

## Slide 5
Program design
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work

## Slide 6
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Calibrate SubVI
Notes: Calibrate (explain process)
For every motor user wants to calibrate:
1) The user identifies the motor to be calibrated on the prompt.
2) The motor is first moved to the negative limit.
3) The motor position is zeroed.
4) Motor position was verified to be zero through read output.
5) The user is prompted to move the motor to a new absolute position.

## Slide 7
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Byte checking loop
Notes: LACK OF TERMINATION CHARACTER
- whole message wasn’t being sent
- point out loop on prev slide
- this piece of code is used everywhereee

## Slide 8
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Snake motion

## Slide 9
Program design
Communication Protocol
  STX + Header + Data + Checksum + ETX
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Establish two-way communication
Format Command

## Slide 10
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Communication Protocol cont.
  STX: 02h
  Header

## Slide 11
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Communication Protocol cont.
  Data: Depends on test (RAD or FLURO)
  Checksum
    complement of STX + Header + Data
    Ex: 02 + 41 + 31 + 43 + 31
    Adding ones and tens separately gives: E8
    Complement(E8) = 17
    Convert to ASCII hex: 31 37
  ETX: 03h
Notes: Give example of previous header

## Slide 12
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Format command: Checksum SubVI

## Slide 13
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Establish two-way communication
  Simple Read/Write vs. Continuous Read/Write

## Slide 14
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Notes: //also video?

## Slide 15
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Notes: //also video?

## Slide 16
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Notes: //also video?

## Slide 17
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Velmex BiSlide Motors
  Creating a Kill Switch
    Pushing “K” command to motor controllers
  Modularizing the snake function
    Modifying bottom-up code
    Repurposing Calibrate SubVI
EMD High Voltage Generator
  Establishing communication
    08D to broadcast (007) destination
    Intercepting messages from CON1
Notes: At the start of each bullet: list the work that has been done so far before going into future improvements

## Slide 18
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work
Acknowledgements
  A special thanks to Dr. Kapadia for letting me work in his lab. I would also like to thank Robert Morris, Manu Lakshmanan, Katie Albanese and James Spencer for their support, and valuable suggestions throughout the work.

## Slide 19: Questions?
Background
Velmex BiSlide
EMD Generator
Final Interface
Future Work